## Slide 1: Integrated label-free PANORAMA and fluorescence imaging for multi-modal exosome analysis
April-7-2021
Pres. By Nareg Ohannesian

## Slide 2: Experimental Details
Exosome used: H460; H460 labelled with PKH67
Antibody for capture: CD63
Experiment duration: 120 min
Concentrations used: 2x103, 2x105 ex/ µl.
Thiol-PEG Biotinylated/methylated: (1:3) 1 mM
Neutravidin: 3.3 µM
Antibody: 50 µg/ml
PKH67:
  Excitation wavelength: 460-490 nm
  Emission wavelength: 500-530 nm
Fluorescence filters:
  Excitation wavelength: 445-490 nm
  Emission wavelength: 500-550 nm
Fluorescence acquisition time: 0.1 sec
H460 derived exosomes
H460 derived exosomes stained with PKH67
Notes: Add acquisition time; increase brightness of overlay.

## Slide 3: Overview
Validation of PANORAMA with fluorescence using fluorescence 100 nm particles
Monitoring the surface functionalization
Monitoring number of exosomes settled with time
Validation of the surface functionalization
Monitoring the number of captured exosomes on anti-CD63 functionalized surface
Determining the non-specific binding in the system

## Slide 4: Part 1: Detection of Carboxylate modified 100 nm polystyrene beads via PANORAMA and fluorescence
PANORAMA
1.165±0.045
Fluorescence
3050±1025
Scale Bar: 8 µm

## Slide 5: Part 2: Full surface functionalization
Bright-field Image of AGNIS immersed in PBS
Neutravidin
2hours
Thiol-PEG Biotin (18 hours)
Anti-CD63
2 hours
Scale Bar: 6 µm

## Slide 6: Evolution of exosome settlement with time
Scale Bar: 4 µm
125 min PANORAMA
50 min PANORAMA
75 min PANORAMA
100 min PANORAMA
25 min PANORAMA
125 min wash PANORAMA
125 min wash Fluorescence
Exosome Concentration 2*10^5 exosomes/µl

## Slide 7: Part 3: Functionalizing AGNIS surface with Thiol-PEG-Biotin
Scale Bar: 6 µm
Time: 15 min
Time: 30 min
Time: 45 min
IR: 1.045+0.026
IR: 1.053+0.022
IR: 1.053+0.023
Notes: Remove?

## Slide 8: Part 1: Functionalization for 60 min to get patches after washing the surface
Neutravidin
Thiol-Peg Biotin 1:3 Thiol-PEG MH
Anti-CD63
Scale Bar: 6 µm
IR: 1.053+0.028
IR: 1.095+0.021
IR: 1.113+0.018

## Slide 9: Part 1: Addition of exosomes
Scale Bar: 6 µm
Functionalized spots
Overlayed images of functionalized spots and exosomes
H460 cell line derived exosomes
Captured: 92; IR: 1.1±0.02
RED: surface functionalization
PINK: Captured Exosome
Exosome conc. 2x10^3 ex/µl
Washed at 60 min

## Slide 10: PANORAMA of H460 derived exosomes on functionalized surface with Anti-CD63 and IgG
Anti-CD63
IgG
Before wash
After wash
After wash
Before wash
91 % of exosomes odf detected exosomes were captured via anti-CD63
3.3 % remained on the surface functionalized with IgG
Scale Bar: 10 µm

## Slide 11: Monitoring the abundance of CD9; CD63 and CD81 surface proteins on cancerous H460 and non-cancerous 293A exosomes
Questions on this part:
Patient samples include various types of exosomes.
This graph is derived using pure exosome solutions thus cannot represent real samples
Can we use this graph to say the abundance of specific surface proteins on H460 and 293A exosomes?
This part does not have fluorescence In it. But if perform immunofluorescence capture (fluorophore labelled antibodies) does it validate our results or do we need a western blot?

## Slide 12: Future work
Finalize the data set of the molecular beacon response for NHBE (0% response) and H460 (80%) exosomes of 25:75; 50:50 and 75:25.
Mixture of 293a and H460 and do antibody tests.
Introduce molecular beacon to plasma samples and see the variation.
Conclusion
PANORAMA is a label free imaging technique which can detect both 100 nm polystyrene beads and exosome particles.
Both particle detection have been validated with fluorescence.
We validate the surface functionalization by detecting them in patches at all stages of surface functionalization